## Slide 1: Smart overnight charging for e-rickshaw garages
ChargeFlow
FIELD FINDINGS · SHIFT HACKATHON · IIT (BHU) VARANASI
What nine drivers in Varanasi told us, and what we built from it.
[Team name] · [Member 1] · [Member 2] · [Member 3]
Notes: About 10 seconds. Say: "We spent a day with e-rickshaw drivers in Varanasi. This is what they told us, and what we built from it." Keep it to one breath; the evidence is the point. Fill in the team name and member names before presenting.

## Slide 2: Owners rent out e-rickshaws and pay for charging
THE PROBLEM
7 of 9
drivers we met rent their e-rickshaw by the day (A, B, C, D, F, G and I). E and H own theirs.
₹380–400 a day
Typical rent, with charging included. The owner supplies the electricity.
About 10 vehicles per garage
They charge together in a small garage that doubles as quarters. Many such garages exist across Varanasi.
Our customer is the garage owner, who carries the electricity bill and, as F told us, the battery replacement.
ChargeFlow · Field findings from Varanasi
02 / 10
Notes: About 30 seconds. Say: seven of the nine drivers rent their vehicle by the day for roughly ₹380–400, and the rent includes charging. So the person who pays the electricity bill is the garage owner, not the driver. They charge about ten vehicles together in a small garage that doubles as quarters, with a room for the drivers. If asked how many garages: we saw a few and heard there are many across Varanasi; we do not have a count. Facts: A, B, C, D, F, G and I rent; E and H own their vehicles. B pays ₹300 rent plus ₹80 charging; G pays ₹300 plus ₹100.

## Slide 3: We spoke to nine drivers in Varanasi, A to I
THE EVIDENCE
Driver | Vehicle | Battery | Full charge | Range | Charging window
A | Rented | Lead-acid | 10 h | 90 km | 8 pm–10 am
B | Rented | Lithium (LFP) | 3–4 h | 100 km | 12 am–11 am
C | Rented | Lithium† | 3.5 h | 100 km | 12 am–10 am
D | Rented | Lead-acid | 8 h | 100 km | 12 am–10 am
E | Own | Lead-acid | 3 h* | 60 km* | At home
F | Rented | Lithium (LFP) | 5–6 h | 100 km | 12 am–11 am
G | Rented | Lead-acid | 8 h | 120 km | 11 pm–8 am
H | Own | Lead-acid | 10 h | 100 km | 11 pm–10 am
I | Rented | Lithium (LFP) | 5 h | 100 km | 10 pm–10 am
* E's pack now gives 60 km (150 km when new) and charges in 3 h (12 h when new). † C reported 8 dry cells (LFP); chemistry to confirm. Figures are as the drivers told us.
ChargeFlow · Field findings from Varanasi
03 / 10
Notes: About 10 seconds on stage, or skip and keep it for questions. Show it as proof of work; do not read it. Sample size is nine drivers, one city, one day, and every figure is as the driver reported it, so treat them as approximate. C reported eight dry cells (LFP); we have not confirmed the chemistry. Drivers A, B, C, D, F, G and I rent; E and H own. Charging windows are the times drivers gave for charging, not meter logs. A and I gave a second window and C also charges 3–7 pm.

## Slide 4: Six of eight drivers start charging between 11 pm and 1 am
FINDING 1
6 pm
12 am
6 am
12 pm
6 pm
A
B
C
D
E
F
G
H
I
Charges at home, time not reported
Overnight window
Daytime top-up (C only)
11 pm to 1 am
Windows as reported. A and I gave a second window, not drawn.
ChargeFlow · Field findings from Varanasi
04 / 10
Notes: About 35 seconds. Say: this is when each driver says charging runs. Six of the eight who gave a window start between 11 pm and 1 am, and nearly all run until 8–11 am. That overlap is what stacks the load on one connection. Caveats to say out loud: these are the charging windows drivers reported, not meter logs; A and I gave a second window that is not drawn; E charges at home and gave no time. C also tops up between 3 and 7 pm, which is daylight, so a lithium driver could charge from solar directly. That is an idea to test, not a finding.

## Slide 5: A third to a half of the ₹400 rent goes on electricity and battery wear
FINDING 2
₹80–100
electricity
₹46–96
battery wear
The rest
vehicle, garage, owner's margin (not measured)
Electricity: ₹80–100 a day
B pays ₹80 on top of ₹300 rent and G pays ₹100 on top of ₹300. H's own meter shows ₹70–80 at home.
Battery: ₹46–96 a day
A set costs ₹48,000–70,000 and is replaced every 1.5 to 3 years, which works out to ₹46 to ₹96 a day.
The owner bears both
Rent includes charging, and F says the owner pays for the battery replacement.
Bar uses midpoints (₹90 + ₹70 = ₹160, about 40%). Derived from the drivers' figures, not the owners' accounts. Battery per day = replacement cost ÷ days between replacements.
ChargeFlow · Field findings from Varanasi
05 / 10
Notes: About 40 seconds. Say: the rent is ₹400 a day and includes charging. Using the drivers' own numbers, electricity is ₹80–100 a day and a battery set of ₹48,000–70,000 replaced every 1.5 to 3 years is ₹46–96 a day. Together that is a third to a half of the rent, and it is the owner's cost. Be clear this is derived from what drivers told us, not from the owners' books. How it was derived: battery per day = replacement cost divided by days between replacements. F: ₹50,000 over 3 years is about ₹46; A and G: ₹48,000 over 2 years is about ₹66; B: ₹70,000 over 2 years is about ₹96. Electricity: B pays ₹80 on top of ₹300 rent, G pays ₹100 on top of ₹300, and H's home meter shows ₹70–80 for 7–8 units. The bar uses midpoints of ₹90 and ₹70, about 40% of the rent; the ranges give 31% to 49%. If asked: we do not know the owner's margin or the garage's own costs.

## Slide 6: Batteries age fast and no one tracks health
FINDING 3
150 → 60 km
Driver E's lead-acid pack: range on a full charge when bought in 2023, and now. Charge time fell from 12 h to 3 h, which fits a pack with far less capacity left.
40%
of the original range is left after about three years (driver E).
1.5–3 years
between battery replacements (A, B, C, E, F, H). E's vehicle company asks for a yearly swap.
Range only
In our notes, battery health is only ever described as km per full charge.
Why it matters: how a pack is charged may change how fast it ages, and retired lithium packs may suit garage storage. Both are hypotheses to test, not findings.
ChargeFlow · Field findings from Varanasi
06 / 10
Notes: About 25 seconds. Say: driver E's pack gives 60 km now against 150 km when the vehicle was bought in 2023, and it charges in 3 hours instead of 12. Every driver described battery health in km per full charge; nobody gave a state-of-health figure. That is why we think battery behaviour matters. The last line is deliberately a hypothesis: charging behaviour may affect ageing, and retired lithium packs may be reusable as garage storage. We have not tested either. Facts behind the right-hand column: E says the vehicle company asks for a replacement every year; A, B and E replace every 2 years; C every 1.5 years; H normally every 1.5 years with a 1-year guarantee; F's last change was 3 years ago.

## Slide 7: In simulation, ChargeFlow stays under the limit
WHAT WE BUILT
Peak grid demand (kW)
10.5 → 6.6
Plug-in-and-charge vs ChargeFlow, against a 7 kW sanctioned load.
Hours over the limit
4.25 → 0
Plug-in-and-charge stays over for 4 h 15 min; ChargeFlow never goes over.
Ready by departure
10 of 10
Plug-in-and-charge also reaches 10 of 10, but only by overloading the building.
At 6 kW, grid only gets 5 of 10 ready. With solar and a second-life pack: 10 of 10.
Solar covers 19% of the night load (5 kW of panels, 15 kWh pack at 75% health, clear sky): a supplement to the grid.
Simulated: 10 rickshaws, 7 kW sanctioned load (assumed), generated arrival and departure times. Not field measurements. We run it live next.
ChargeFlow · Field findings from Varanasi
07 / 10
Notes: About 45 seconds here, then 60–90 seconds of live demo. Say: ChargeFlow is software that decides, every 15 minutes, which chargers are switched on so the building stays under its sanctioned load, and switches each charger off when its pack is ready. All numbers on this slide come from our simulator with a 7 kW limit we assumed and generated arrival and departure times; they are not field measurements. Be upfront that plug-in-and-charge also reaches 10 of 10 at 7 kW, but only by running 4 hours 15 minutes over the limit. Then switch to the live app: pick the scenarios, drop the sanctioned load to 6 kW, and show grid only at 5 of 10 against solar and storage at 10 of 10. Solar covers 19% of the night load with 5 kW of panels, so present it as a supplement. Numbers if asked: peak 10.5 kW uncontrolled vs 6.6 kW; 11.7 kWh less grid energy with solar and storage than grid only.

## Slide 8: Five things we have not verified yet
HONEST SCOPE
What we have not verified | Why it matters
Sanctioned load and breaker trips at a garage | Our central claim is that ten chargers exceed the connection. The visit did not ask this.
Charger rating, and whether it cuts off when full | Sets the real load per vehicle and how much energy float charging wastes.
Energy per charge: 7–8 units from H, one driver | The simulator assumes about 5 kWh per vehicle, so it may understate the load.
Whether the garage connection is residential | Decides if PM Surya Ghar rooftop solar can apply. Even a 3 kW system gives about 12 kWh a day, against 70–80 kWh of nightly charging if H's figure holds.
The "morning charging" subsidy we heard about | Unclear whether it is a tariff or a purchase subsidy. Either could change the owner's electricity cost.
ChargeFlow · Field findings from Varanasi
08 / 10
Notes: About 25 seconds. Say: this is what we do not know yet. The visit did not ask about breaker trips or the sanctioned load, and that is the heart of our claim, so we are treating it as unverified and will ask an owner. The brief itself says one honest sentence beats a confident guess. Be ready to explain the numbers: H reported 7–8 units a day costing ₹70–80 at home, which is about ₹10 a unit; check that against a bill. 10 vehicles at 7–8 units would be 70–80 kWh a night, against about 12 kWh a day from a 3 kW system at roughly 4 kWh per kW, so solar can only be a supplement. The subsidy note in our field report said the government provides a subsidy for e-rickshaws "in the morning to charge"; we could not tell whether that means a time-of-day tariff or something else.

## Slide 9: Next: measure one garage for a week
NEXT
Week 1
Measure
Put smart plugs on one garage's chargers: real kW, start and stop times, meter readings.
Week 2
Calibrate
Replace our assumed pack, charger and household figures with the measured ones.
Week 3
Trial
Run the schedule on some chargers and compare it with the owner's usual night.
After
Solar and second life
Check the connection type and PM Surya Ghar eligibility, and test retired lithium packs as storage.
Proposed plan; it depends on a garage owner agreeing.
[Team name] · [Member 1: role] · [Member 2: role] · [Member 3: role]
ChargeFlow · Field findings from Varanasi
09 / 10
Notes: About 20 seconds. Say: the next step is to measure, not to scale. Smart plugs on one garage for a week would give real kW per charger and real start and stop times; then we replace our assumptions with those numbers and trial the schedule on a few chargers. This is a proposal and depends on an owner agreeing, so say so. Fill in the team line with names and roles before presenting, and finish by thanking the room and offering the live demo again for questions.

## Slide 10: Field data against our simulator
BACKUP
Parameter | Simulator assumed | Drivers reported | What we do about it
Plug-in time | Arrivals 19:30–23:30, mean about 21:30 | Charging starts 11 pm–midnight for six of eight | Shift the model later; ask if drivers plug in before charging starts
Departure time | 05:30–08:00; simulation ends at 09:00 | 8–11 am | Extend the simulation to 11:00
Charge time | Lead-acid about 8.5–9.8 h; lithium not modelled | Lead-acid 8–10 h; lithium 3–6 h | Matches for lead-acid; add a lithium option
Energy per vehicle | About 5 kWh from the grid per night | 7–8 units a day (H, one driver) | Confirm with a meter reading
Sanctioned load | 7 kW placeholder | Not collected | Ask a garage owner
ChargeFlow · Field findings from Varanasi
10 / 10
Notes: For questions only. Two corrections we owe the simulator: plug-in times should be later (the model's mean arrival is about 21:30, while most drivers say charging starts between 11 pm and midnight), and the simulation window should run to about 11 am, because drivers leave between 8 and 11 am and the current window ends at 09:00. Lead-acid charge time in the model matches what drivers reported. Offer to open the Fleet data tab, where arrival and departure times and starting charge can be edited live, so any figure a judge questions can be changed on the spot.